## Slide 1: CL321: Petroleum Refinery Engineering Module-1

## Slide 2: Module 1
Exploration and refining of crude oil

## Slide 3: What is petroleum?
The word petroleum is derived from the Latin words for rock (petra) and oleum (oil).
It is found in the form of gas and/or liquid phases in porous rock structures.
Both gases and liquids are rich mixtures of organic components consisting of carbon and hydrogen and hence are known as hydrocarbons in general. Usually, these are available in the sub-surface of Earth in the porous rocks known as sedimentary basins.
In the majority of the basins, gas, oil, and water coexist under pressure with methane gas at the cap and oil is sandwiched between the gas and water.

## Slide 4: OIL DISCOVERY
Oil was discovered by chance.
When man first began to seek petroleum the easiest way to find it was to look for evidence of oil seeps on the earth’s surface.
Oil seeps are result of seepage from along a fracture.
Observation of seeps has lead to the discovery of many of the word’s great oil field in U.S., middle-east, Venezuela and at other places.

## Slide 5
HISTORY
World’s first oil well was drilled in Titusville, Pennsylvania, USA by Drake in 1859
As long as 3000 B.C. Persians used Asphaltic pitch for illuminating purpose.
Sperm oil ( obtained from whale) used in lamps in early 18th century become short supply
Initial discoveries were all near leaking oil and gas on ground.

## Slide 6: CRUDE OIL EXPLORATION HISTORY OF INDIA
The first explorers looked for gold dust at the confluence of Brahmaputra and Dhansiri rivers and not for oil
First oil well in India was drilled in Makum in Assam in 1866 just seven years after the famous ‘Drake and colleague’ drilled the first crude oil in the year 1859.
The well was completed at a depth of 662 ft with initial production of 200 gallons/day in Nov-1890

## Slide 7: Crude Oil Exploration History of India
After Independence, India’s first well, on a “concealed structure’ covered under the Allyuvium was drilled in Naharkatiya which struck oil in 1953. This was followed by Moran in 1956 both in Assam.
ONGC after its formation in 1956 first struck gas in Cambay in 1958 and oil in Ankleshwar in 1960. During sixties, it discovered three major fields namely Rudrasagar, Lakwa and Geleki in Assam.

## Slide 8: CRUDE OIL EXPLORATION HISTORY OF INDIA
The most remarkable event in the country’s oil exploration history is the discovery of Bombay High field of 1974. Subsequently, many oil and gas fields have been discovered in Bombay, Cambay, Assam, Krishna, Godavari and Cauvery. The last major discovery was Gandhar in 1984.
Oil India Limited (OIL) after being formed in 1959, primarily developed the discovered fields –Naharkatiya and Moran. In recent years discoveries from deeper depths in Assam. It explored Mahanadi and Saurashtra offshore without success. It is currently exploring in parts of Ganga and Rajasthan basins also.

## Slide 9
CRUDE OIL EXPLORATION HISTORY OF INDIA
Prior to drilling of Digboi # 1, a number of shallow wells were drilled in Makum-Namdang area based on the geological work and oil seepages carried out by B.Medlicott of GSI
In 1899, a new company was promoted and named as Assam Oil Company (AOC)
In 1901 Digboi Refinery was Commissioned
Digboi field was passed onto Burmah Oil Company in 1921, by this time 80 wells were completed with average production of 350 bopd.
**one barrel is exactly 158.987294928 litres.

## Slide 10
CRUDE OIL EXPLORATION HISTORY OF INDIA
In 1953, big oil strike in Naharkatiya followed by discovery of big subsurface structures at Rudrasagar and Geleki in 1954 and discovery of oil in Moran in 1956 by AOC in Assam changed the energy scenario of India
In 1955, Oil and Natural Gas Division was setup under GSI by GOI
In May 1956, this Division was converted to Oil & Natural Gas Directorate
Directorate was converted to Commission on 14th August 1956

## Slide 11
CRUDE OIL EXPLORATION HISTORY OF INDIA
1958
In 1958, ONGC stuck gas in Jawalamukhi and oil in well Cambay # 1
1959
In 1959, ONGC became autonomous statutory body

## Slide 14: Three Basic Rock Types
The earth’s crust is composed of three basic rock types: igneous, sedimentary and metamorphic.
Igneous rocks are formed from the crystallization of molten rock (magma or lava) from within the earth’s mantle. Common igneous rocks include granite, basalt, and gabbro.
Metamorphic rocks are formed from pre-existing rocks by mineralogical, chemical and/or structural changes in response to marked changes in temperature, pressure, shearing stress, and chemical environment. These changes generally take place deep within the earth’s crust. Examples of common metamorphic rocks include slate, marble and schist.
Sedimentary rocks are formed as sediments, either from eroded fragments of older rocks or chemical precipitates. Sediments lithify by both compaction, as the grains are squeezed together into a denser mass than the original, and by cementation, as minerals precipitate around the grains after deposition and bind the particles together. Sediments are compacted and cemented after burial under additional layers of sediment. Thus sandstone forms by the lithification of sand particles and limestone by the lithification of shells and other particles of calcium carbonate. These types of rocks are typically deposited in horizontal layers, or strata, at the bottom of rivers, oceans, and deltas. Limestone, sandstone, and clay are typical sedimentary rocks

## Slide 15: Petroleum-Bearing Rocks
Sedimentary rocks are the most important and interesting type of rock to the petroleum industry because most oil and gas accumulations occur in them; igneous and metamorphic rocks rarely contain oil and gas.
All petroleum source rocks are sedimentary.
Furthermore, most of the world’s oil lies in sedimentary rock formed from marine sediments deposited on the edges of continents. For example, there are many large deposits that lie along the Gulf of Mexico and the Persian Gulf.

## Slide 21: Shales
Shale is a type of detrital sedimentary rock formed by the consolidation of fine-grained material including clay, mud, and silt and have a layered or stratified structure parallel to bedding. Shales are typically porous and contain hydrocarbons but generally exhibit no permeability. Therefore, they typically do not form reservoirs but do make excellent cap rocks. If a shale is fractured, it would have the potential to be a reservoir.

## Slide 22: Formation of Shale Oil Shale
Oil is formed from organic-rich shale, which acts as both the source rock and the reservoir rock.
Step-by-Step Formation Process
Deposition of Organic Matter-Millions of years ago, microscopic plants and organisms (plankton, algae) settled at the bottom of marine or lacustrine environments. These environments were low-energy and oxygen-poor, preventing decomposition. Fine sediments (clay and silt) settled along with organic matter, forming organic-rich mud.
Burial and Compaction-Over geological time, additional sediments buried the organic-rich layers. Pressure increased, and the material compacted to form shale. Organic matter transformed into kerogen.
Thermal Maturation (Heating): With increasing depth, temperature rises due to the geothermal gradient. At temperatures of approximately: 60–120°C → Oil window >120°C → Gas window. Kerogen breaks down into liquid hydrocarbons (shale oil) and natural gas.
Retention Within Shale Unlike conventional reservoirs, shale has very low permeability. Generated hydrocarbons do not migrate far. Oil remains trapped within: Nanopores, Organic matter pores, Microfractures.
Thus, shale serves as both source rock and reservoir.

## Slide 23: Shale oil

## Slide 25: Formation of crude oil
To date, it is generally agreed that crude petroleum oil was formed from decaying plants and vegetables and dead animals and converted to oil by the action of high pressure and high temperature under the earth’s surface, and by the action of the biological activities of micro-organisms.
Organic materials of plant or animal origin accumulate in the lowest places, usually in the crevices, low-lying land, sea bed, coral reefs, etc., and are gradually buried under the surface of Earth. Thus, huge amounts of organic matter are trapped layer after layer in the earth’s crust and rock. Rocks that bear these organic layers are called sedimentary rocks. Several kilometers below the earth’s surface, organic sediments are decayed biologically to a mass, known as kerogen, which has a very high mass of organic-to-inorganic ratio favorable for conversion to hydrocarbon.
The temperature of Earth increases with depth (geothermal gradient) at the rate of approximately 30°C per kilometer. Thus, at a depth of 4–5 km, called kitchen by geologists, temperatures of 120°C–150°C exist where kerogen is converted to hydrocarbon oil under very high pressure of rocks and soil. But this conversion takes millions of years (geological time period) to complete.
Methane is also formed thermogenically (i.e., thermal conversion of kerogen) along with biogenic methane already present before the formation of crude oil.
Migration of oil with gas occurs within the rock layers by the pressure gradient from high to low pressure zones. The formation of crude (or crude deposit) oil has been found in the sedimentary porous rock layers trapped under the hard and impervious igneous rock layers. Crude oil and gas accumulate in the pores of the sedimentary rocky layer as shown in next Figure. This formation may be found from a few kilometers (as deep as 2 km and as deep as 7 km) below the earth’s surface.

## Slide 27: What are Oil and Gas?
Oil and Gas are substances found within the earth’s crust.
They are thought to come from decomposed plant and animal matter.
Scientists believe the plants and animals died long ago, and were slowly buried by thick layers of sediments. Over a long period of time, and with pressure and temperature, the organic materials were converted into the oil and gas which are found today.
(For example, we know that present day garbage dumps give off methane gas)
** On average, the temperature increases by about 25°C for every kilometer of depth

## Slide 29: Variation of pressure with depth in earth

## Slide 30: What else do we know about Oil and Gas?
Oil in it’s natural state can be thick or thin, black or light colored.
When oil is refined, many products can be obtained:
  Energy for power
  Gasoline for cars
  Diesel fuel for trucks and trains
  Hi-octane fuels for vehicle
  Heating oil for houses
Many other materials also come from petroleum:
Plastics
Materials for clothes (example: polyester fabrics)
Chemicals for everyday use
Paints

## Slide 31: Oil Reserves in India
India holds 4,728,790,000 barrels of proven oil reserves as of 2016, ranking 24th in the world and accounting for about 0.3% of the world's total oil reserves of 1,650,585,140,000 barrels. India has proven reserves equivalent to 2.9 times its annual consumption. This means that, without imports, there would be about 3 years of oil left (at current consumption levels and excluding unproven reserves).

## Slide 32: India Oil
 | Barrels | Global Rank
Oil Reserves | 4,728,790,000 | 24th in the world
 | Barrels per Day | Global Rank
Oil Production | 1,016,371 | 20th in the world
Oil Consumption | 4,443,000 | 3rd in the world
Daily Deficit | -3,426,629 | 
Oil Imports | 4,255,300 | 
Oil Exports | 5 | 
Net Imports | 4,255,295 | 

## Slide 33: Oil Consumption in India
India consumes 4,443,000 barrels per day (B/d) of oil as of the year 2016.
India ranks 3rd in the world for oil consumption, accounting for about 4.6% of the world's total consumption of 97,103,871 barrels per day.
India consumes 0.14 gallons of oil per capita every day (based on the 2016 population of 1,324,517,249 people), or 51 gallons per capita per year (1 barrels). [1 barrel = 42 US Gallons]

## Slide 34: Oil Production in India
India produces
1,016,370.64 barrels per day of oil (as of 2016) ranking 20th in the world.
India produces every year an amount equivalent to 7.8% of its total proven reserves (as of 2016).
Oil Imports:
India imports 96% of its oil consumption (4,255,295 barrels per day in 2016).

## Slide 36: World oil reserve

## Slide 37: Oil EXPLORATION TECHNIQUES
Visible evidence of a hydrocarbon source, like seepage of oil and gas from the surface, the visual appearance of surface and vegetation, the presence of oil or gas in fountains or rivers, lakes etc.
Modern exploration techniques use geophysical, geochemical, and geotechnical methods.
Geophysical methods involves gravimetric, magnetometric, seismic, radioactive, and stratigraphic studies of the surface.
Chemical analysis of the surface soil and rocks are
carried out by geochemical methods.
Geotechnical methods, such as the mechanical properties of rocks and surface, are measured.
Remote sensing from satellite is the most recent development for a low cost geological survey

## Slide 38
GRAVIMETRIC METHOD:
Gravity of the earth’s surface varies with distance from the surface of Earth and the type of material, such as salt, water, oil, gas, or mineral matter.
Porous and oil-containing rock layers and salt have lower density compared to the surrounding non-porous and hard rock layers. Thus, a gravimetric curve is acquired and analyzed for the location of deposit

## Slide 39
MAGNETOMETRIC METHOD:
Earth has its own magnetic field that varies from one location to another owing to the different structural materials of rocks and also the presence of solar-charged particles received by Earth.
A variation of magnetic field strength is recorded by a sensitive instrument, called a magnetometer.
Igneous non-porous rocks are found to be magnetic as compared to sedimentary rocks containing organic deposits.
Both the gravimetric and magnetometric methods are done simultaneously to predict a reproducible sub-surface structure.
After the zone is confirmed by gravimetric and magnetometric surveys, a seismic survey is carried out for a clear image of the sub-surface structure.

## Slide 40
SEISMIC SURVEY:
This technique uses a sonic instrument over a desired site to correctly locate the prospective basin structure. In this method, a sound signal generated by the explosion method (explorers call them mini-earthquakes, which are artificially created by explosives) is transmitted through the earth’s surface under study and reﬂected signals are detected by geophones located at specified positions.
The frequency and time of the reﬂected signal varies with the density, porosity, and the type of reﬂecting surface.
Various rock deposits at different depths vary with density and porosity.
Seismic reﬂection can measure this change as it travels below the surface.
Computer simulation software is used for imaging the sub-surface structure. This is applied to all the surveys for fast and accurate prediction about the oil and gas reserve location

## Slide 41
REMOTE SENSING METHOD:
Solar radiation from the Earth’s surface varies in intensity and frequency depending on the sub-surface property.
This observation is collected via satellite to predict the sub-surface structure. In order to image the sub-surface structure, historical geological data collected previously by gravimetric, magnetometric, and seismic surveys are used.
The final image is obtained by geological imaging software (GIS). However, the remote sensing method is not applicable during nighttime or places incapable of reﬂecting solar radiation, like the ocean surface, which absorbs substantial amounts of solar radiation.
However, extrapolation from the land surface in the vicinity of the sea can be accurately predicted, but is not applicable for the deep sea area.
A radioactive or gamma-ray survey is also used in the exploration.

## Slide 42
GEOCHEMICAL METHODS:
Inorganic contents of surface or shallow cuttings or core are sampled and analyzed for inorganic materials, such as salts and carbonates, which are frequently associated with hydrocarbons.
Organic contents or the presence of organic matter is detected by heating a sample in a crucible and the loss of mass of the sample is an indication of the presence of organic matter.
The ratio of organic mass to inorganic matter in a sample is used to ascertain the presence of hydrocarbons. Total organic carbon is defined as the carbon present in the organic matter in the sample which is different in inorganic carbon from carbonates.
Core samples are examined for porosity, permeability, salt content, organic content, and many other physical and chemical properties.

## Slide 43
STRATIGRAPHY:
Correlations are established between wells, fossils, rock and mud properties, before and during drilling operations for the final prediction, and this technique is known as stratigraphy. But it is important to remember that prediction from exploration may not be correct as far as the location and amount of deposit are concerned.
It may happen that the drilling operation may not yield oil or the yield may not be sufficient at the explored site and that the expenditure borne by this work is irrecoverable.

## Slide 44: MODULE 1

## Slide 45: Boiling Points
Methane (CH₄): -162°C [Lowest]
Ethane (C₂H₆): -89°C
Propane (C₃H₈): -42°C
Butane (C₄H₁₀): -1°C
Pentane (C₅H₁₂): 36°C
Hexane (C₆H₁₄): 69°C
Heptane (C₇H₁₆): 98°C
Octane (C₈H₁₈): 126°C
Nonane (C₉H₂₀): 151°C
Decane (C₁₀H₂₂): 174°C
Undecane (C₁₁): 196°C
Dodecane (C₁₂): 216°C
Hexadecane (C₁₆): 287°C
Eicosane (C₂₀): 343°C

## Slide 46: Boling point of various hydrocarbons (alkanes, olefins and aromatics)
Carbon Atoms | n-Alkane (°C) | 1-Alkene (°C) | Cycloalkane (°C) | Aromatic (°C)
C1 | Methane: -162 | Ethene: -104 | Cyclopropane: -33 | Benzene: 80
C2 | Ethane: -89 | Ethene: -104 | Cyclobutane: 13 | Toluene: 111
C3 | Propane: -42 | Propene: -48 | Cyclopentane: 49 | Ethylbenzene: 136
C4 | Butane: -1 | 1-Butene: -6 | Cyclohexane: 81 | o-Xylene: 144
C5 | Pentane: 36 | 1-Pentene: 30 | Cycloheptane: 119 | m-Xylene: 139
C6 | Hexane: 69 | 1-Hexene: 63 | Cyclooctane: 151 | p-Xylene: 138
C7 | Heptane: 98 | 1-Heptene: 94 | Cyclononane: 179 | n-Propylbenzene: 159
C8 | Octane: 126 | 1-Octene: 121 | Cyclodecane: 201 | Cumene: 152
C9 | Nonane: 151 | 1-Nonene: 147 |  | Mesitylene: 165
C10 | Decane: 174 | 1-Decene: 171 |  | Naphthalene: 218

## Slide 47: BP of Alkenes
Ethene (C₂H₄): -104°C
Propene (C₃H₆): -48°C
1-Butene (C₄H₈): -6°C
1-Pentene (C₅H₁₀): 30°C
1-Hexene (C₆H₁₂): 63°C
1-Heptene (C₇H₁₄): 94°C
1-Octene (C₈H₁₆): 121°C
1-Nonene (C₉H₁₈): 147°C
1-Decene (C₁₀H₂₀): 171°C
Higher MW → Higher BP
Rule: +CH₂ group → +20-30°C increase

## Slide 48: ALKYNES - CₙH₂ₙ₋₂
Ethyne (acetylene): -84°C (sublimes)
Propyne: -23°C
1-Butyne: 8°C
1-Pentyne: 40°C
1-Hexyne: 71°C
2-Butyne: 27°C (higher than 1-butyne)
Reason: Terminal alkynes have acidic H, weaker interactions

## Slide 49: CYCLOALKANES (NAPHTHENES) - CₙH₂ₙ
Cyclopropane (C₃): -33°C
Cyclobutane (C₄): 13°C
Cyclopentane (C₅): 49°C
Cyclohexane (C₆): 81°C
Cycloheptane (C₇): 119°C
Cyclooctane (C₈): 151°C
Cyclononane (C₉): 179°C
Cyclodecane (C₁₀): 201°C

## Slide 50: AROMATIC HYDROCARBONS Monocyclic Aromatics:
Benzene (C₆H₆): 80°C
Toluene (C₇H₈): 111°C
Ethylbenzene (C₈H₁₀): 136°C
o-Xylene (1,2-dimethyl): 144°C
m-Xylene (1,3-dimethyl): 139°C
p-Xylene (1,4-dimethyl): 138°C
Cumene (isopropylbenzene): 152°C
n-Propylbenzene: 159°C
Mesitylene (1,3,5-trimethyl): 165°C
Butylbenzene: 183°C

## Slide 51: C₆ Compounds Comparison:
Hexane (C₆H₁₄): 69°C [Lowest]
1-Hexene (C₆H₁₂): 63°C
Cyclohexane (C₆H₁₂): 81°C
Benzene (C₆H₆): 80°C
C₈ Compounds Comparison:
n-Octane (C₈H₁₈): 126°C
1-Octene (C₈H₁₆): 121°C
Cyclooctane (C₈H₁₆): 151°C
o-Xylene (C₈H₁₀): 144°C
Ethylbenzene (C₈H₁₀): 136°C

## Slide 52: Crude chemistry
Fundamentally, crude oil consists of 84 – 87 wt % carbon, 11 – 14 % hydrogen, 0 – 3 wt % sulphur, 0 – 2 wt % oxygen, 0 – 0.6 wt % nitrogen and metals ranging from 0 – 100 ppm.

## Slide 53: BASE OF A CRUDE OIL
Crude oil comprises different types of hydrocarbon e.g., paraffinic, naphthenic, aromatic and cyclic . Depending upon the predominance of a particular group of hydrocarbons, crude oil may be classified into:-
Paraffinic Base
Intermediate or Mixed Base
Naphthenic Base

## Slide 54: Paraffins
Paraffins refer to alkanes such as methane, ethane, propane, n and iso butane, n and iso pentane.

## Slide 56: Olefins
Alkenes such as ethylene, propylene and butylenes are highly chemically reactive. They are not found in mentionable quantities in crude oil but are encountered in some refinery processes.

## Slide 57: Naphthenes
Naphthenes or cycloalkanes such as cyclopropane, methyl cyclohexane are present in the crude oil.
These compounds are not aromatic and hence do not contribute much to the octane number.
In the reforming reaction, these compounds are targeted to generate aromatics which have higher octane numbers than the naphthenes.

## Slide 58: Aromatics
Aromatics such as benzene, toluene, o/m/p-xylene are also available in the crude oil. These contribute towards higher octane number products and the target is to maximize their quantity in a refinery process

## Slide 59: Napthalene
Polynuclear aromatics such as naphthalenes consist of two or three or more aromatic rings.

## Slide 60: Organic Sulphur
Organic Sulphur compounds such as thiophene, pyridine also exist in the crude oil. The basic difficulty of these organic sulphur compounds is the additional hydrogen requirements in the hydrotreaters

## Slide 62: Oxygen containing compounds
These compounds do not exist 2 % by weight in the crude oil. Typical examples are acetic and benzoic acids. These compounds cause corrosion and therefore needs to be effectively handled.

## Slide 65: Resins
Resins are polynuclear aromatic structures supported with side chains of paraffins and small ring aromatics. Their molecular weights vary between 500 – 1500. These compounds also contain sulphur, nitrogen, oxygen, vanadium and nickel.

## Slide 66: Asphaltenes
Asphaltenes are polynuclear aromatic structures consisting of 20 or more aromatic rings along with paraffinic and naphthenic chains. A crude with high quantities of resins and asphaltenes (heavy crude) is usually targeted for coke production.

## Slide 68: Sulphur Content, wt%
The sulfur content varies from less than 0.5% to greater than 5%.
Typically, crude oil Sulphur content consists of 0.5 – 5 wt % of Sulphur. Crudes with Sulphur content lower than 0.5 wt % are termed as sweet crudes. It is estimated that about 80 % of world crude oil reserves are sour.
Crudes with greater than 0.5% sulphur generally require more extensive processing than those with lower sulphur content

## Slide 69: Salt Content, lb/1000 bbl
If the salt content of the crude, when expressed as NaCl, is greater than 10 lb/1000 bbl, it is generally necessary to desalt the crude before processing.

## Slide 70: Important characterization properties of crude and its products
Numerous important feed and product characterization properties in refinery engineering include
True boiling point (TBP) curve
ASTM distillation curve
API gravity
Watson Characterization factor
Viscosity
Sulfur content
Pour point
Flash and fire point

## Slide 71: True Boiling point(TBP) Distillation (ASTM D-285 distillations are the tests most commonly used)
This type of distillation is commonly used due to the accuracy of the results obtained by this method which is very close to that obtained via real distillation or industrial distillation. In this distillation, there is a fractionation column located between the condenser and the flask.
In general, this type of distillation is carried out by two steps: firstly, under atmospheric pressure until 300°C (1% distilled every 2 min),
Secondly under vacuum pressure (to prevent cracking process and to reduce the boiling point) at 40mmHg (1% distilled every 3-5 min). In this process, the vapor press. temp. is plotted vs. distilled(%) to get TBP curve.
There is a trend toward using the results of a 15:5 distillation (D-2892) rather than the TBP. The 15:5 distillation is carried out using 15 theoretical plates at a reflux ratio of 5:1.

## Slide 74: ASTM distillation
In this type of distillation there is on fractionation column located between the condenser and the flask. On the other hand, the raised vapor will not be fractionated in this process. This distillation is used with fractions having short range of the boiling point.

## Slide 75: Equilibrium Flash Vaporization (EFV)
This is a single stage separation technique. A liquid mixture feed is pumped through a heater to raise the temperature and enthalpy of the mixture.
It then flows through a valve and the pressure is reduced, causing the liquid to partially vaporize. Because the vapor and liquid are in such close contact up until the "flash" occurs, the product liquid and vapor phases approach equilibrium.

## Slide 76: Average Boiling Points
in prediction of physical properties and characterization of hydrocarbon mixtures a single characteristic boiling point is required.
Generally an average boiling point for a fraction is defined to determine the single characterizing boiling point. There are five average boiling points defined by the following equations, Three of these average boiling points are VABP (volume average boiling point), MABP (molal average boiling point) and WABP (weight average boiling point), defined for a mixture of n components as
where ABP is the VABP, MABP, or WABP and xi is the corresponding volume, mole, or weight fraction of component i

## Slide 77: Average Boiling Point

## Slide 80: Problem
A low boiling naphtha has the ASTM D 86 temperatures of 77.8, 107.8, 126.7, 155, and 184.4°C at 10, 30, 50, 70, and 90 vol% distilled [11]. Calculate VABP WABP MABP, CABP, and MeABP for this fraction.

## Slide 81: Yield curve and Cut Points
Using a crude TBP curve, cut points are defined as the temperatures that represent the limits of a distillate fraction.
For example, for kerosene, fraction Ta represents the lower cut point, and Tb represents the upper cut point.
Boiling ranges between the cut points represent distillate products, such as naphtha, kerosene, light gas oil, etc. The difference between the cumulative volume percent at upper and lower cut points is reported as the yield (in volume %) for the particular distillate fraction. For example, for the crude represented in Figure, the kerosene yield can be calculated as 40%(at Tb) -20% (Ta) = 20% by volume.

## Slide 82: Distillation curves

## Slide 83: Interconversion of Various Distillation Data
Riazi-Daubert Method
General equation
where Ti (available) is the available distillation temperature at a specific vol% distilled and Ti (desired) is the desired distillation data for the same vol% distilled, both are in kelvin. SG is the specific gravity of fraction at 15.5°C and a, b, and c are correlation parameters specific for each conversion type and each vol% point on the distillation curve.
Ti (available) is ASTM temperature at 10% and Ti (desired) is the EFV temperature at 10%

## Slide 84: ASTM D 86 and TBP Conversion
If distillation data available are in the form of ASTM D 86 and desired distillation is TBP, the previous Equation can be used, but for this particular type of conversion value of constant c for all points is zero and the equation reduces to
average absolute deviation (AAD) of about 5°C

## Slide 86: ASTM D 86 and EFV Conversions
EFV = a(ASTM D 86)b(SG)c
where constants a, b, and c were obtained from more than 300 data points and are given in Table 3.3
average absolute deviation (AAD) of 6°C

## Slide 87: Specific gravity estimation
In using these equations if specific gravity of a fraction is not available, it may be estimated from available distillation curves at 10% and 50% points as given by the following equation:
Where, constants a, b, and c for the three types of distillation data, namely, ASTM D 86, TBP, and EFV, are given in Table 3.4. Temperatures at 10 and 50% are both in Kelvin.

## Slide 88: Daubert's Method
In these methods, first conversion should be made at 50% point and then the difference between two cut points are correlated in a form similar to Eq. (3.14).
ASTM and TBP Conversion-The following equation is used to convert an ASTM D 86 distillation at 50% point temperature to a TBP distillation 50% point temperature.
where ASTM (50%) and TBP (50%) are temperatures at 50% volume distilled in kelvin.
Equation (3.20) can also be used in a reverse form to estimate ASTM from TBP.
The following equation is used to determine the difference between two cut points

## Slide 89: Correlation constants for Eq. (3.21).

## Slide 90
To determine the true boiling point temperature at any percent distilled, calculation should begin with 50% TBP temperature and addition or subtraction of the proper temperature difference Yi
This method was developed based on samples with ASTM 50% point temperature of less than 250°C (480°F but it is recommended for extrapolation up to fractions with ASTM 50% temperature of 315°C (600°F as suggested by the API.)
Average absolute deviation for this method as reported by the API-TDB is about 4.6°C for some 70 samples.
Predicted TBP at 0 and 100% are the least accurate values followed by values at 10% and 90% points.

## Slide 94: Assignment 2
Convert the given ASTM D 86 Data to TBP data using Riazi-Daubert and Daubert methods. Also calculate AAD

## Slide 95: CRUDE OIL PROPERTIES
Density :
° API Gravity
specific gravity and ° API gravity refer to the weight per unit volume at 60°F as compared to water at 60°F
The lighter the oil, the larger the API gravity
  °API < 22 Heavy oil
  22< ° API <31.1 Medium oil
  °API>31.1 Light oil

## Slide 96: Pour Point, °F(°C)
The lower the pour point, the lower the paraffin content and the greater the content of aromatics

## Slide 97: Carbon Residue, wt%
Carbon residue is determined by distillation to a coke residue in the absence of air.
The carbon residue is roughly related to the asphalt content of the crude and to the quantity of the lubricating oil fraction that can be recovered.
In most cases the lower the carbon residue, the more valuable the crude.
This is expressed in terms of the weight percent carbon residue by either the Ramsbottom (RCR) or Conradson (CCR) ASTM test procedures (D-524 and D-189)
Carbon residue is a measure of the coke-forming tendencies of oil. It is determined by destructive distillation in the absence of air of the sample to a coke residue. The coke residue is expressed as weight percent of the original sample. There are two standard ASTM tests, Conradson carbon residue (CCR) and Ramsbottom carbon residue (RCR).
Conradson carbon: A test used to determine the amount of carbon residue left after the evaporation and pyrolysis of an oil under specified conditions. Expressed as weight percent; ASTM D-189.
Ramsbottom carbon: A measure of the carbon forming potential (amount of coke formed) of a petroleum fraction. This is determined by a standard laboratory test procedure which subjects the sample to severe thermal cracking conditions. Recommended to replace Conradson carbon; ASTM D-524. Carbon residue expressed in wt% of the original sample.

## Slide 98: Characterization Factors
UOP or Watson ‘‘characterization factor’’ (KW) and the U.S. Bureau of Mines ‘‘correlation index’’ (CI) are defined as
The Watson characterization factor ranges from less than 10 for highly aromatic materials to almost 15 for highly paraffinic compounds. Crude oils show a narrower range of KW and vary from 10.5 for a highly naphthenic crude to 12.9 for a paraffinic base crude.
The correlation index is useful in evaluating individual fractions from crude oils. The CI scale is based upon straight-chain paraffins having a CI value of 0 and benzene having a CI value of 100.
The CI values are not quantitative, but the lower the CI value, the greater the concentrations of paraffin hydrocarbons in the fraction; and the higher the CI value, the greater the concentrations of naphthenes and aromatics

## Slide 99: Characterization Factor
CF < 10.5 -aromatic based
between 10.5 to 12.9: naphthenic based
CF between 12.9 to 15 -paraffinic based
CF Above 15 - highly paraffinic based

## Slide 100: Nitrogen Content, wt%
organic nitrogen compounds cause severe poisoning of catalysts used in processing and cause corrosion problems
Crudes containing nitrogen in amounts above 0.25% by weight require special processing to remove

## Slide 101: Metals Content, ppm
The metals content metals (nickel, vanadium, and copper) of crude oils vary from a few parts per million to more than 1000 ppm.
Can cause poison to catalyst
Vanadium concentrations above 2 ppm in fuel oils can lead to severe corrosion to turbine blades and deterioration of refractory furnace linings and stacks.

## Slide 102: Boiling range and %yield of petroleum products

## Slide 103: Composition of Crude Oils

## Slide 105: Testing methods for crude oil and its products
For crude oil
Distillation

## Slide 106: IBP
The temperature of vapour giving the first drop of condensate is reported as the initial boiling point (IBP).

## Slide 108: Liquified Petroleum Gas
Liquefied petroleum gas (LPG) is a mixture of propane and butane in liquefied form at a pressure of about 10–15 atm
weathering test: In this test, 100 mL of liquid LPG is kept in a test tube with a mercury-in-glass thermometer dipped into it. Liquid LPG starts vaporizing through the open mouth of the test tube to the atmosphere, causing the temperature to fall rapidly. After 95mL of liquid is vaporized, the residual liquid temperature is noted.
If the temperature is very low (below 0°C), then the proportion of propane in the mixture is more in mixture.
if it is high (above 2°C), then the proportion of butane will be more

## Slide 109: Copper strip corrosion test
a standard polished copper strip is dipped into liquid LPG in a thick-walled small vessel, known as a bomb, kept at a constant temperature, usually 30°C.
After 1 hr, the bomb is opened and the copper strip is removed and compared its brightness of surface against a set of standard copper strips indicating different degrees of corrosion.
The presence of mercaptans and hydrogen sulfide causes corrosion to vessels, pipelines, and joints.

## Slide 111: Reid’s vapour pressure test
Domestic LPG has a maximum RVP of 8 kg/cm2 at a temperature of 37.8°C

## Slide 112: Important parameters as per the Indian Bureau of Standard (BIS) of LPG

## Slide 113: KEROSENE
Smoke Point
The smoke point is determined as the height of the flame (in millimeters) produced by oil in the wick of a stove or a lamp without forming any smoke
Domestic kerosene should have a smoke point of 20 mm (minimum)
Smoke forming can be attributed to presence of aromatics

## Slide 114: Smoke point

## Slide 115: Flash Point
The flash point is defined as the temperature of the oil at which it momentarily flashes in presence of air and the igniting source.
For domestic kerosene, it should not be below the ambient temperature. In India, this value is 35 °C (minimum)

## Slide 116: Closed cup flash point/fire point apparatus

## Slide 117: Open cup flash point/fire point apparatus

## Slide 118: Char Point and Bloom
Char point is defined as the coke and ash left on the wick after complete burning of the oil.
For domestic kerosene, the maximum amount of char allowed is 20 mg/kg of oil burnt.
Bloom is the darkness produced by the flame of the oil while burning in a standard glass. The bloom should not be darker than a standard brightness desired in a lamp.

## Slide 119: Distillation Test
ASTM distillation of kerosene is carried out under atmospheric conditions. Finished kerosene must be at least 20% distilled at 200°C or lower and the final boiling point (FBP) should be no more than 300°C.
Kerosene that is too light is dangerous for use in a domestic kerosene stove as explosion may occur owing to the presence of a very light boiling fraction especially in the range of naphtha.
The presence of too heavy boiling fractions in kerosene will make it a poorly burning fuel.

## Slide 120: Sulfur Content and Corrosion
Since sulfur produces hazardous sulfur dioxide, kerosene must be free from it.
Domestic kerosene must not have a sulfur content of more than 0.25% by weight.
A corrosion test of kerosene is also carried out using the copper strip corrosion method

## Slide 121
Summary: Kerosene

## Slide 122: Test methods of Motor spirit
ASTM D86 distillation

## Slide 123: Testing

## Slide 124: ASTM D86 distillation curve for MS (American society for testing and materials)

## Slide 125: OCTANE NUMBER
Octane number is defined, for any MS fuel, as the percentage of iso-octane in a mixture of iso-octane and n-heptane, which will give the same engine performance (CFR: Co-operative fuel research engine) as could be achieved by the actual fuel sample.

## Slide 126: Octane number
Research Octane number (RON)-measured at 600 rpm
Motor octane number-measured at 900 rpm
Additives added to enhance octane no.-methyl tertiary butyl ether, ethyl tertiary butyl ether, Tetra ethyl lead (TEL, now banned)

## Slide 127: Corrosion
Presence of mercaptan sulfur may cause corrosion in the fuel pipes and the engine cylinder and produce sulfur dioxide during combustion.
Catalytic mercaptan oxidation method treatment to convert mercaptan to disulfides.
Nowadays mercaptans and other sulfur compounds are mostly removed by hydrodesulphurization.

## Slide 128: Reid Vapour Pressure
RVP of MS should not exceed 0.7 kg/cm2 (gauge) .
High vapour pressure will give rise to problems vapour locking in the engine and vapour loss.
Too low vapour pressure will give rise to problems starting the engine.

## Slide 129: Oxidation Stability
MS is a mixture or blend of hydrocarbons obtained from refinery, such as
reformate (obtained from a naphtha reforming plant),
thermally (viscosity breaking unit, coking unit, etc.),
catalytically cracked gasoline components (from a fluidized bed catalytic cracking unit).
By-products from petrochemical plants, like aromatics and pyrolysis gasoline components
There is possibility to contain some undesired olefins which may polymerization when contacted with oxygen.
These polymerized products make layers of films or gum like substances and reduce the effectiveness of the fuel while used
This gum formation is a slow process but may cause severe damage to fuel if stored for a long time
This is tested in the laboratory by contacting fuel and oxygen (or air) in a pressure vessel at a constant temperature for a specified period (usually 6 h or longer) and a fall in pressure

## Slide 130: HIGH SPEED DIESEL

## Slide 131: Cetane number
Paraffinic hydrocarbon has a lower autoignition temperature than that of aromatics.
If diesel oil is rich with aromatic hydrocarbons than the paraffinic counterparts, most of the oil will be unburnt at the beginning and will simultaneously burn suddenly when the temperature rises due to the combustion of paraffinic hydrocarbons.
Cetane no. - percentage of normal cetane (a straight chain hydrocarbon) in a mixture of n-cetane and α-methyl naphthalene (an aromatic hydrocarbon), which gives the same performance as that of the diesel sample. This is tested in a standard diesel engine of CFR.

## Slide 132: Diesel Index
DI = °API × aniline point in °F ∕ 100
value of the DI should be at least 45
DI is directly proportional to the cetane number

## Slide 133: Sulfur content
The sulfur content should not be more than 0.25% by weight of the oil

## Slide 134: Corrosion test
A corrosion test of diesel is also carried out using the copper strip method at 100°C for 3 h

## Slide 135: Pour Point
pour point is defined as the temperature at which oil will cease to flow due to the formation of wax crystals.
In India, the pour point of diesel has been fixed at a value less than 6°C.

## Slide 136: Viscosity
It should be between 2.5 and 7 centistoke (cSt*) at 38°C
*1 stokes = 100 centistokes = 1 cm2 s−1 = 0.0001 m2 s−1.

## Slide 137: Important parameters as per BIS of Diesel

## Slide 138: Carbon Residue, wt%
Carbon residue is determined by distillation to a coke residue in the absence of air. The carbon residue is roughly related to the asphalt content of the crude and to the quantity of the lubricating oil fraction that can be recovered. In most cases the lower the carbon residue, the more valuable the crude. This is expressed in terms of the weight percent carbon residue by either the Ramsbottom (RCR) or Conradson (CCR) ASTM test procedures (D-524 and D-189).

## Slide 139
Conradson (CCR) apparatus

## Slide 140: VISCOSITY INDEX
Proposed by Dean and Davis.
The viscosity index (VI) is an empirical parameter that indicates the rate of change of the viscosity of the oil due to a variation in temperature.
The oil which changes its viscosity rapidly with temperature, is having low viscosity index. An oil with minimum change in viscosity with temperature has high VI.
Viscosity index is defined as the ratio of the difference of viscosity (U) of the lube oil to be used with respect to the viscosity (L) of petroleum (aromatic/naphthenic) oil having zero VI to the difference of viscosity (H) of high VI oil (paraffinic; 100 VI) to the viscosity (L) of zero VI oil for a temperature change from 40°C to 100°C.
U = kinematic viscosity at 40°C of the oil whose viscosity index is to be calculated mm2/s (cSt).
kinematic viscosity at 40°C of an oil of 0 viscosity index having the same kinematic viscosity at 100°C as the oil whose viscosity index is to be calculated, mm2/s (cSt)
kinematic viscosity at 40°C of an oil of 100 viscosity index having the same kinematic viscosity at 100°C as the oil whose viscosity index is to be calculated mm2/s (cSt).
Viscosity of the sample and reference oils must be so selected that they have the same viscosity at 100°C.
Pennsylvanian paraffinic oil of a selected type which shows a desirable , relatively small change of viscosity with change in temperature, were assigned as a VI of 100. Selected Texas coastal oil shows less desirable viscosity-temperature characteristics were assigned as VI of 0.

## Slide 141: Viscosity index

## Slide 142: Viscosity index

## Slide 143
In the case when the VI, calculated as above, is greater than 100 the following relation is applicable for calculating the VI as
OR
If the kinematic viscosity is above 70 mm2/s (cSt) at 100°C, calculate the values of L and H as follows:
Y = kinematic viscosity at 100°C of the oil whose viscosity index is to be calculated, mm2/s (cSt),

## Slide 144
Hydrocarbon | Viscosity | Viscosity index | Pour point
Paraffins | Low | High | High
Naphthenes | Medium | Low | Low
aromatics | High | Low | Low

## Slide 145: Total acid number
The total acid number (TAN) is a measurement of acidity that is determined by the amount of potassium hydroxide in milligrams that is needed to neutralize the acids in one gram of oil.
The TAN value indicates to the crude oil refinery the potential of corrosion problems.
It is usually the naphthenic acids ( cyclopentyl and cyclohexyl carboxylic acids ) in the crude oil that cause corrosion problems.

## Slide 146: AVIATION FUELS
Gasoline based for jet fuel- Aviation gasoline is usually polymer gasoline or alkylated gasoline having an octane number greater than 100.
Kerosene based for turbine fuel-Kerosene based aviation fuel is known as aviation turbine fuel (ATF) and is mostly consumed by passenger aeroplanes. This fuel is the hydrocarbon fraction boiling in the range of 190–250°C and is similar to the kerosene fraction.

## Slide 148: FURNACE FUELS
GASEOUS FUELS
Off-gases and by-product gases commonly generated in refineries and petrochemical plants consist of methane, ethane, propane, butane, and their olefinic homologues.
LIQUID FUELS Light diesel oil or LDO (much heavier than HSD) is a liquid fuel. It is usually a blend of vacuum gas oil, coker gas oil, deasphalted oil, waxy distillates, etc., and falls into the category of black oil.

## Slide 149: LDO

## Slide 150: Furnace oil or fuel oil
Obtained from viscosity broken crude residue and vacuum distillates and is commonly used as the cheapest furnace oil in industrial furnaces. It is a black petroleum oil with higher viscosity

## Slide 151: Internal fuel oil (IFO)
It is predominantly a mixture of asphalt, short residue, and wax.

## Slide 152: LUBRICATING OIL
A lubricant is a solid, semi-solid, or liquid material that is used to reduce friction between two solid surfaces.
Examples -- graphite, sulfur, wax, soap, and mineral oil.
Lubricating oils are liquid lubricants mainly made from petroleum oils (lube oil base stocks) blended with soaps of fatty acids and other additives.
The main ingredients are petroleum base stocks that are obtained from vacuum distillates of crude oil. These distillates are heavy petroleum fraction and cannot be vaporized like petrol or diesel.

## Slide 154: MISCELLANEOUS PRODUCTS
JUTE BATCHING OIL
Obtained from the atmospheric crude distillation unit.
Boiling fraction slightly different from that of diesel cut and it is 340°C–365°C.
Jute Batching Oil in the jute industry to make the jute fibers pliable.
Oils are used in the jute industry for processing and baling jute fibres.

## Slide 155: MINERAL TURPENTINE OIL (MTO)
boiling range of 125°C–240°C.
C7 to C12 hydrocarbon with aliphatic and alicyclic compounds
This cut is obtained directly from the crude distillation unit as a straight run product or by splitting kerosene cut.
Used in the paint industry as a solvent or thinner

## Slide 156: MTO

## Slide 157: CARBON BLACK FEED STOCK
Carbon black feed stock (CBFS) is a petroleum product rich in aromatics suitable for yielding carbon particles or coke for battery and metallurgical industries. It is a by-product from a lube extraction plant where aromatic hydrocarbons from distillate oil are removed as an extract. The resulting aromatic rich oil after recovery of the solvent is obtained as the CBFS.

## Slide 158: BITUMEN
Asphalt or bitumen is obtained from short residue (residual mass from the bottom of the vacuum distillation unit) after extraction of valuable oil (known as bright stock) by propane. Asphalt is a very sticky, semi-solid, viscous petroleum, containing various hetero-atomic compounds of hydrocarbons enriched with metallic, sulfurous, nitrogenous, and oxygenated compounds. At a temperature above 90°C, it flows like liquid and solidifies at room temperature. It is mainly used as paving material, paint, water-proofing agent, etc.

## Slide 159: Bitumen

## Slide 160: PETROLEUM COKE
Petroleum residue (preferably vacuum residue) contains heavy hydrocarbons that crack at high temperature in the absence of air yielding gases, light hydrocarbon liquids, and black solid carbon rich residue or coke.
The greater the amount of heavy aromatic hydrocarbons in the feed stock, the greater the yield of coke
Thermal cracking of petroleum involves various reactions, like decomposition, dehydrogenation, isomerization, polymerization yield coke.
Main use of this coke in metallurgical industry.

## Slide 161: WAX
Solvent-treated vacuum distillates and deasphalted oil are further treated to adjust the pour point of the oil.
Normal paraffinic hydrocarbons present in the oil have a high solidification temperature and form wax as the solid or semi-solid mass of hydrocarbons. There are paraffinic molecules that can solidify even at room temperature.
Since lubricating oil is used at various temperatures, ranging from very low to very high temperatures, it is essential that lubricating oil does not solidify in this range of temperatures.
Wax-forming hydrocarbons are selectively removed by low temperature freezing and separation.
This is usually carried out by mixing the feed oil with a solvent, such as methyl ethyl ketone, benzene, or toluene, mixed in various proportions to prevent crystallization of the wax-forming molecules in the precoolers and chillers, until they are separated from the solvents along with the desired oil components through a filter.
Wax is obtained from the refinery as a by-product from a de-waxing unit
Petroleum hydrocarbons that solidify at a temperature above −20°C.
High molecular weight normal paraffinic hydrocarbons are the major constituent of wax.
Vacuum distillates usually contain much wax and are removed by freezing at low temperature.
Paraffinic wax is usually available as a slack wax, whereas naphthenic wax is available as microcrystalline wax
Slack wax is soft and has a low melting point suitable for candle making, paper coating, etc.
Microcrystalline wax is hard with a high melting point and has a variety of applications, such as cosmetics, paints, and as an additive in rubber and plastics.